## Slide 1
Time-Varying
Fields

## Slide 2: Boundary Conditions

## Slide 3: Electric vs Magnetic Comparison
G.L.
← A.L.
Conservative →
Field lines form closed loops

## Slide 5
Time-Varying Fields
Time-Varying Fields
Stationary charges electrostatic fields
Steady currents magnetostatic fields
Time-varying currents electromagnetic fields
Only in a non-time-varying case can electric and magnetic fields be considered as independent of each other. In a time-varying (dynamic) case the two fields are interdependent (coupled). A changing magnetic field induces an electric field, and vice versa.

## Slide 6
Time-Varying Fields
The Continuity Equation
Electric charges may not be created or destroyed (the principle of conservation of charge).
Consider an arbitrary volume V bounded by surface S. A net charge Q exists within this region. If a net current I flows across the surface out of this region, the charge in the volume must decrease at a rate that equals the current:
Divergence theorem:
This equation must hold regardless of the choice of V, therefore the integrands must be equal:
For steady currents
that is, steady electric currents are divergenceless or solenoidal.
Kirchhoff’s current law
follows from this
the equation of
continuity
Partial derivative because may be a function of both time and space
This equation must hold regardless of the choice of V, therefore the integrands must be equal:

## Slide 7
Time-Varying Fields
Displacement Current
For magnetostatic field, we have
Taking the divergence of this equation we find that
However, the continuity equation (accounting for time variation) requires that
Thus we must modify the magnetostatic curl equation to agree with the continuity equation. Let us add a term to the former so that it becomes
where is the conduction current density, and is to be determined and defined.

## Slide 8
Time-Varying Fields
Displacement Current (continued)
Taking the divergence we have
In order for this equation to agree with the continuity equation,
displacement current density
Stokes’ theorem
Gauss’ law

## Slide 9
A typical example of displacement current is the current through a capacitor when an alternating voltage source is applied to its plates. The following example illustrates the need for the displacement current.
To resolve the conflict we need to include in Ampere’s law.
Time-Varying Fields
Displacement Current (continued)
Using an unmodified form of Ampere’s law:
(no conduction current flows through ( =0))
S1
S2

## Slide 10
Time-Varying Fields
Displacement Current (continued)
The total current density is .In the first equation so it remains valid. In the second equation so that
So we obtain the same current for either surface though it is conduction current in and displacement current in .
Q
Charge +Q
Charge -Q
I
Surface S1
Path L
Path L
Surface S2
I
Charge +Q
Charge -Q

## Slide 11: Electric vs Magnetic Comparison
G.L.
← A.L.
Conservative →
Field lines form closed loops

## Slide 12
Time-Varying Fields
Faraday’s Law
Faraday discovered experimentally that a current was induced in a conducting loop when the magnetic flux linking the loop changed. In differential (or point) form this experimental fact is described by the following equation
Taking the surface integral of both sides over an open surface and applying Stokes’ theorem, we obtain
where is the magnetic flux through the surface S. Examples: transformer, etc.
Time-varying electric field is not conservative (voltage between two points may be not unique).
Induced emf v(t) depends on B, S, cosθ and their rate of change. Also on the number of turns N:
Integral form

## Slide 13
For A = (10 × 10) cm2 , V = 100 V
13
Maximum rate-of-change of current (dI/dt)
Lightning induced effects are often related to dI/dt
According to Faraday’s Law:
Lightning Parameters vs. Damage Mechanisms
r = 2 m
dI/dt = 100 kA/µs
(for A = 1 m2)
Area A
H = I/2πr (Ampere’s law)
dH/dt = (dI/dt)/2πr
dB/dt = μ0(dH/dt)
= μ0(dI/dt)/2πr
Notes: 13

## Slide 14
Time-varying electric field is not conservative
Suppose that there is only one unique voltage . Then
Time-Varying Fields
Faraday’s Law (continued)
However,
Thus can be unambiguously defined only if (in practice, if than the dimensions of system in question)
Path L1
B
A
Path L2
The effect of electromagnetic induction. When time-varying magnetic fields are present, the value of the line integral of from A to B may depend on the path one chooses (the larger the area, the larger the difference).

## Slide 15
Time-Varying Fields
Faraday’s Law (continued)
According to Faraday’s law, a time-varying magnetic flux through a loop of wire results in a voltage across the loop terminals:
The negative sign shows that the induced voltage acts in such a way as to oppose the change of flux producing it (Lenz’s law).
Induced magnetic field (when circuit is closed)
1
2
3
4
The terminals are far away from the time-varying magnetic field
Increasing time-varying
magnetic field
-
+
Direction of the integration path
R
I
A time-varying magnetic flux through a loop wire results in the appearance of a voltage across its terminals.
Consider now terminals 3 and 4, and 1 and 2
1
2
3
4
Integration path
No contribution from 2-3 and 4-1 because the wire is a perfect conductor
If N-turn coil instead of single loop

## Slide 16
Time-Varying Fields
Faraday’s Law continued
Example: An N-turn coil having an area A rotates in a uniform magnetic field The speed of rotation is n revolutions per second. Find the voltage at the coil terminals.
Shaft
Rotation
rad
B = const
A = const

## Slide 17
Time-Varying Fields
Inductance
A circuit carrying current I produces a magnetic field which causes a flux to pass through each turn of the circuit. If the medium
surrounding the circuit is linear, the flux is proportional to the current I producing it .
For a time-varying current, according to Faraday’s law, we have
Self-inductance L is defined as the ratio of the magnetic flux linkage to the current I.
, H (henry)
Magnetic field B produced by a circuit.
-
+
I
I
(voltage induced across coil)

## Slide 18
Time-Varying Fields
Inductance (continued)
In an inductor such as a coaxial or a parallel-wire transmission line, the inductance produced by the flux internal to the conductor is called the internal inductance Lin while that produced by the flux external to it is called external inductance
Let us find of a very long rectangular loop of wire for which , and . This geometry represents a parallel-conductor transmission line. Transmission lines are usually characterized by per unit length parameters.
h
w
Wire radius = a
I
Finding the inductance per unit length of a parallel-conductor transmission line.
( )
1
S

## Slide 19: Inductance (cont’d) The magnetic field produced by each of the long sides of the loop is given approximately by
The internal inductance for nonferromagnetic materials is usually negligible compared to .
Parallel–conductor transmission line
, H/m (per unit length)
(Ampere’s Law)

## Slide 20: Inductance (cont’d) Let us find the inductance per unit length of a coaxial transmission line. We assume that the currents flow on the surface of the conductors, which have no resistance.
Finding the inductance per unit length of a coaxial transmission line.
h
I
b
a
z

## Slide 21
Time-Varying Fields
Inductance (continued)
Since R=0, has only radial component and therefore the segments 3 and 4 contribute nothing to the line integral.
(from previous work, for lossless TLs)
It follows that v(z)-v(z+h) = Lh(dI/dt)
H/m
Resistance
Lossless coaxial
transmission
line
Faraday’s
Law
Voltage drop
between z
and z+h
v(z)-v(z+h)

## Slide 22
By applying Kirchhoff’s voltage law to N - (N + 1) - (N + 1)’ - N’ loop, we obtain
If node N is at the position z, node (N +1) is at position z + h, and
Definitions of currents and voltages for the lumped-circuit lossless transmission-line model.
Transmission Lines
(slide 5)
N’
(N+1)’
iNS

## Slide 23
Boundary Condition on Tangential Electric Field
Using Faraday’s law, , we can obtain boundary condition on the
tangential component of at a dielectric boundary.
Time-Varying Fields
(For the normal component: )
at a dielectric boundary
Medium 2
Medium 1
L
L
(unless )
continuous across the boundary, which also applies to a conductor/dielectric boundary
3
1
Et1l – Et2l = 0

## Slide 24
24
Electric Fields in the Immediate Vicinity of the Lightning Channel Core
Vertical and horizontal (radial) components of electric field in the immediate vicinity (within 0.1 to 1.6 m) of the triggered-lightning channel were measured with Pockels sensors at Camp Blanding, Florida, in 2000 (Miki et al., 2002)

## Slide 25
25
Vertical electric field, E(t), measurements in the immediate vicinity (within 0.1 to 1.6 m) of the lightning channel (Miki et al. 2002) and current, I(t), measurements at the channel base were used to estimate power per unit length, P(t) = E(t) I(t), as a function of time (up to 50 s). Integrating this power over time, we obtained lightning input energy per unit length. The implication here is that the vertical electric field within 0.1 to 1.6 m of the lightning channel is not much different from the longitudinal electric field inside the channel.
E(t)
I(t)
Lightning channel
r
Lightning input energy is needed in a number of areas including the determination of NO produced by lightning and the testing of proposed thunder generation mechanisms. There is presently no consensus on the energy associated with the lightning return stroke (103 to 105 J/m).
Estimation of Input Energy in Rocket-Triggered Lightning Strokes

## Slide 26
General Forms of Maxwell’s Equations
Differential Integral Remarks
Gauss’ Law
Nonexistence
of isolated magnetic charge
Time-Varying Fields
Faraday’s Law
Ampere’s
Law
In 1 and 2, S is a closed surface enclosing the volume V
In 2 and 3, L is a closed path that bounds the surface S
1
2
3
4

## Slide 27
Time-Varying Fields
Electric fields can originate on positive charges and can end on negative charges. But since nature has neglected to supply us with magnetic charges, magnetic fields cannot begin or end; they can only form closed loops.

## Slide 28
Time-Varying Fields
Sinusoidal Fields
In electromagnetics, information is usually transmitted by imposing amplitude, frequency, or phase modulation on a sinusoidal carrier. Sinusoidal (or time-harmonic) analysis can be extended to most waveforms by Fourier and Laplace transform techniques.
Sinusoids are easily expressed in phasors, which are more convenient to work with. Let us consider the “curl H” equation.
Its phasor representation is
is a vector function of position, but it is independent of time. The three scalar components of are complex numbers; that is, if
then

## Slide 29
Time-Varying Fields
Sinusoidal Fields (continued)
Time-Harmonic Maxwell’s Equations Assuming Time Factor .
Point Form Integral Form

## Slide 30
Time-Varying Fields
Maxwell’s Equations (continued)
Electromagnetic flow diagram showing the relationship between the potentials and vector fields: (a) electrostatic system, (b) magnetostatic system, (c) electromagnetic system. [Adapted with permission from IEE Publishing Department]
“Free magnetic charge density” ( )
Electrostatics
Magnetostatics
Electrodynamics
(c)
(b)
Ampere’s Law
Faraday’s Law
(a)

## Slide 31
Time-Varying Fields
Sinusoidal Fields (continued)
Time-Harmonic Maxwell’s Equations Assuming Time Factor .
Point Form Integral Form

## Slide 32
Time-Varying Fields
The Electromagnetic Skin Effect
When time-varying fields are present in a material that has high conductivity, the fields and currents tend to be confined to a region near the surface of the material. This is known as the “skin effect”. Skin effect increases the effective resistance of conductors at high frequencies.
Let us consider the vector wave equation (Helmholtz’s equation) for the electric field:
If the material in question is a very good conductor, so that , we can write
Consider current flowing in the +x direction through a conductive material filling the half-space z<0. The current density is independent of y and x, so that we have
Since
we also have:
Magnitude of current density decreases exponentially with depth
(Air) Z>0
(Metal) Z<0
Current density at surface J0
Skin depth
x
z
y
0

## Slide 33
Time-Varying Fields
The Skin Effect (continued)
As , the first term increases and would give rise to infinitely large currents. Since this is physically unreasonable, the constant A must vanish. From the condition when z=0 we have
and
At
At
Skin depth versus frequency for copper
Current density magnitude decreases exponentially with depth. Its phase changes as well.
10mm
1mm
0.1mm

## Slide 34
Time-Varying Fields
Time-Varying Fields
Surface Impedance
or
“ohms per square”
Illustrating the concept of “ohms per square”
If l=w (a square surface)
Direction of current flow
w
l
45° out of phase with Jo
Surface impedance
Voltage per unit length
If , the total current per unit width is
Since we can write

## Slide 35
RS is equivalent to the dc resistance per unit length of the conductor having cross-sectional area
Time-Varying Fields
Surface Impedance (continued)
For a wire of radius α,
Copper

## Slide 36
Time-Varying Fields
Time-Varying Fields
Surface Impedance (continued)
Wire (copper) bond
Plated metal connections
Substrate
Z=?
(a)
(b)
(c)
Finding the resistance and internal inductance of a wire bond. The bond, a length of wire connecting two pads on an IC, is shown in (a). (b) is a cross-sectional view showing skin depth. In (c) we imagine the conducting layer unfolded into a plane.
100 μm
δ = 0.6 μm
x 100 μm
w
2 r
Thickness of current layer = 0.6 μm = δ
(Internal inductance)

## Slide 37
Time-Varying Fields
The Skin Effect (continued)
Skin Depth and Surface Resistance for Metals
Metal |  | A | B
Silver |  |  | 
Copper |  |  | 
Gold |  |  | 
Aluminum |  |  | 
Iron |  |  |