## Slide 1
1
1. Types of Lightning Discharges and Lightning Terminology
Notes: 1

## Slide 2
Terminology
Lightning
Lightning Discharge
Lightning Flash
Flash
Lightning Strike - lightning discharge to an object (grounded or ungrounded) or to ground
Lightning Bolt – a non-technical term for lightning

## Slide 3
3
3
An isolated thundercloud in the central New Mexico, with rudimentary indication of how electric charge is thought to be distributed and around the thundercloud, as inferred from the remote and in situ observations. Adapted from Krehbiel (1986).
Cloud Charge Structure
← Positive corona at ground
Rain drops →
Notes: 3
3.1

## Slide 4
Types of lightning discharges from cumulonimbus (thunderclouds)
Cloud-to-ground (25%)
Cloud-to-air
Intracloud
Cloud-to-
cloud
Cloud discharges (75%)
4
Types of Lightning Discharges and Lightning Terminology
4
Notes: 4

## Slide 5
Lightning, as any electric discharge, converts air (σ = 10-14 S/m at sea level) to ionized gas or plasma. Such conversion occurs when the electric field exceeds the electric breakdown threshold, 30 kV/cm (at sea level).

## Slide 6
Beasley, W. H. anf Jordan, D. M. "Comparison of High-Speed Video and VHF Source Locations for CG Lightning Flashes", AGU 2008, AE24A-02. Photron, 10,000 frames per second (100-µs frames).
6
Δ
Δ
Notes: 6

## Slide 7
Four types of lightning effectively lowering cloud charge to ground. Only the initial leader is shown for each type. In each lightning-type name given below the sketch, the direction of propagation of the leader and the polarity of the cloud charge effectively lowered to ground (not polarity of the initial leader) are indicated.
Types of Lightning Discharges: CGs
7
Notes: 7

## Slide 8
8
Downward Negative Lightning Discharges to Ground (-CGs)
The total lightning flash duration is typically about 0.2 s (maximum about 1-2 s)
Each flash is usually composed of
two or more component strokes
(or just strokes)
Stroke = Leader/Return-Stroke Sequence (duration of some ms to tens of ms)
Notes: 8

## Slide 9
Diagram showing the luminosity of a three-stroke ground flash and the corresponding current at the channel base: (a) still-camera image, (b) streak-camera image, and (c) channel-base current.
SL = Stepped Leader; DL = Dart Leader; RS = Return Stroke
Downward Negative Lightning Discharges to Ground
9
There may be surges superimposed on continuing current, which are called M-components.
Notes: 9

## Slide 10
Location (Reference) | Average Number of Strokes per Flash | Percentage of Single-Stroke Flashes | Sample Size
New Mexico (Kitagawa et al., 1962) | 6.4 | 13% | 83
Florida (Rakov and Uman, 1990) | 4.6 | 17% | 76
Sweden (Cooray and Perez, 1994) | 3.4 | 18% | 137
Sri Lanka (Cooray and Jayaratne, 1994) | 4.5 | 21% | 81
Brazil (Ballarotti et al., 2012) | 4.6 | 17% | 883
Arizona (Saraiva et al., 2010) | 3.9 | 19% | 209
Malaysia (Baharudin et al., 2014) | 4.0 | 16% | 100
Number of strokes per negative flash and percentage of single-stroke flashes.

## Slide 11
11
A lightning flash that appears to have at least seven (perhaps as many as 10) separate ground strike points: (a) still-camera photograph, (b) moving-camera photograph. Some of the strike points are associated with separate branches of the same stroke while others associated with the fact that different strokes may take different paths to ground. The first and second strokes exhibit unconnected branches. The second and third strokes, second and third from the right on the streaked photograph, are brighter that the first stroke, on the far right. Adapted from Hendry (1993).
t
Multiple Channel Terminations on Ground
Notes: 11

## Slide 12
12
Multiple Channel Terminations on Ground
Notes: 12

## Slide 13
13
Number of Channel Terminations per Flash
Location (Reference) | Average Number of Channels per Flash | Percentage of Multigrounded Flashes | Sample Size
New Mexico (Kitagawa et al., 1962) | 1.7 1.6 | 49% 42% | 72* 83**
Florida (Rakov and Uman, 1990) | 1.7 | 50% | 76
Arizona (Valine and Krider, 2002) | 1.4 | 35% | 386
France (Berger et al., 1996; Hermant, 2000) | 1.5 | 34% | 2995
Brazil (Saraiva et al., 2010) | 1.7 | 51% | 138
Arizona (Saraiva et al., 2010) | 1.7 | 48% | 206
* multiple-stroke flashes only
** including 11 single-stroke flashes assumed to have single channel per flash
Notes: 13

## Slide 14
14
Histogram of the distances between the multiple terminations of 22 individual ground flashes in Florida. The distances were determined using optical triangulation and thunder ranging. Adapted from Thottappillil et al. (1992).
Multiple Channel Terminations on Ground
Min = 0.3 km
Max = 7.3 km
GM = 1.7 km
Thunderstorms
typically move
at 40 km/hr or
4 km in 6 min, but
bolts-from-the-blue can occur.
Notes: 14

## Slide 15
15
Bolt-from-the-blue
VHF source image of a negative bolt-from-the-blue discharge, superimposed on a vertical radar scan through the storm. The lightning began as an upward intracloud discharge between mid-level negative charge (red sources) and upper positive charge (blue sources), then exited the cloud and went to ground as a negative leader, well away (about 5 km) from the storm. The ‘triangle’ denotes the negative cloud-to-ground strike point. Adapted from Krehbiel et al. (2008).

## Slide 16: High-speed video of the bolt-from-the-blue obtained at the Lightning Observatory in Gainesville (LOG), Florida

## Slide 17
Ground Surface Arcing
17
Photograph of surface arcing associated with the second stroke (current peak I = 30 kA) of flash 9312 triggered at Fort McClellan, Alabama (Rg = 260 Ω). One of the surface arcs approached the right edge of the photograph, a distance of 10 m from the rocket launcher. Adapted from Fisher et al. (1994). V = I x Rg = 7.8 MV
10 m
Main lightning channel is outside the field of view
Notes: 17

## Slide 18
18
Ground Surface Arcing
Single vertical ground rod 0.3 or 1.3 m long in heavy red clay (Rgr = 260 )
Percentages of return strokes producing optically detectable surface arcing as a function of return-stroke current peak (Fort McClellan, Alabama, 1993 and 1995). The numbers above each histogram column indicate the number of strokes producing optically detectable arcing (numerator) and the total number of strokes in that current peak range (denominator). Adapted from Rakov et al. (1998).
Notes: 18

## Slide 19
Cloud Charge Distribution
Preliminary
Breakdown
Stepped
Leader
Attachment
Process
First Return
Stroke
Dart
Leader
K and J Process
t = 0
1.00 ms
1.10 ms
1.20 ms
19.00 ms
20.00 ms
20.10 ms
20.20 ms
40.00 ms
60.00 ms
61.00 ms
62.05 ms
A drawing illustrating various processes comprising a negative cloud-to-ground lightning flash (continuing current and M-components are not shown here). Adapted from Uman (1987, 2001).
Second Return
Stroke
Downward Negative Lightning Discharges to Ground
19
Notes: 19

## Slide 20
Dart Leader
Return Stroke
Continuing
Current
M Component
Schematic representation of current versus height profiles for three modes of charge transfer to ground in negative lightning subsequent strokes: (a) dart leader/return stroke sequence, (b) continuing current, and (c) M-component. The corresponding current versus time waveform represents current at the ground. Adapted from Rakov et al. (2001).
Downward Negative Lightning Discharges to Ground
20
Notes: 20

## Slide 21
Channel Characteristics | Pre-Dart-Leader Channel (Ahead of Dart-Leader Front) | Pre-Return-Stroke Channel (Behind Dart-Leader Front and Ahead of Return-Stroke Front) | Return-Stroke Channel (Behind Return-Stroke Front) | Common Streamer Zone in Rocket-Triggered Lightning
Temperature, K | ~ 3000 | ≥ 20,000 | ≥ 30,000 | ~ 300
Conductivity, S/m | ~ 0.02 | ~ 104 | ~ 104 | 3 x 10-5
Radius, cm | ~ 3 | ~ 0.3 | ~ 3 | 2.5 m
R, Ω/m | ~ 18,000 | ~ 3.5 | ~ 0.035 | 1,700
Estimated characteristics of the lightning channel associated with various processes of the lightning discharge
For comparison, the electrical conductivity of carbon is 3 x 104 S/m, of seawater is 4 S/m, and of copper is 5.8 x 107 S/m (Sadiku, 1994); the temperature of solar interior is 107 K, of solar surface is 6000 K, and the temperatures at which tungsten and lead melt are 3600 K and 600 K, respectively (Halliday and Resnick, 1974).

## Slide 22
Negative Downward Lightning - Summary
The majority (80% or more) of cloud-to-ground lightning flashes are composed of two or more strokes. The average number of strokes per flash is typically 3 to 5.
One-third to one-half of lightning flashes create two or more terminations on ground separated by up to several kilometers. When only one location per flash is recorded, the correction factor for measured values of Ng to account for multiple channel terminations on ground is about 1.5-1.7.
Each stroke is composed of a leader, charging the channel, and a return stoke, neutralizing the leader charges. Return-stroke peak currents range from a few kiloamperes to a few hundreds of kiloamperes.
There are three modes of charge transfer to ground: leader/return stroke sequence, continuing current, and M component.
22
Notes: 22

## Slide 23
23
Upward Lightning Initiated by Ground-Based Objects
Notes: 23

## Slide 24
Four types of lightning effectively lowering cloud charge to ground. Only the initial leader is shown for each type. In each lightning-type name given below the sketch, the direction of propagation of the leader and the polarity of the cloud charge effectively lowered to ground (not polarity of the initial leader) are indicated.
Types of Lightning Discharges: CGs
24
Notes: 24

## Slide 25
25
Diagram showing the luminosity of an upward negative flash and the corresponding current at the channel base: (a) Still-camera image, (b) streak-camera image, and (c) channel-base current.
UPL = Upward Positive Leader; ICC = Initial Continuous Current; UPL + ICC = Initial Stage (IS) Current; DL = Dart Leader; RS = Return Stroke
Lightning Initiated by Ground-Based Objects
25 to 50 %
contain return
strokes
Notes: 25

## Slide 26
Streak photograph of stroke 3 in a flash that occurred in Gainesville, Florida on 10 August 1982. the image on the left is due to the dart leader, and the brighter image on the right is due to the return stroke. Adapted from Jordan et al. (1997).
Return
stroke
Dart
leader
← Ground termination point
1
2
3
1 – 3,000 K
R = 18 kΩ/m
2 – 20,000 K
R = 3.5 Ω/m
3 - >30,000 K
R = 0.035 Ω/m
Nonlinearity of lightning channel
Notes: 26

## Slide 27
03.8.2001 06:58:24
Imax = 20 kA
Q tot = 129 C
14 pulses (some of them superimposed on slowly-varying current)
Courtesy of Dr. G. Diendorfer
100 ms
27
Notes: 27

## Slide 28
Monte San Salvatore Tower (70 m), Lugano, Switzerland
28
Courtesy of Prof. R.E. Orville, Texas A&M
Notes: 28

## Slide 29
29
Upward Lightning Initiated by Ground-Based Objects
Canary Wharf (London)
Empire State
(New York)
Petronas Towers
(Kuala Lumpur)
Sears Tower (Chicago)
Taipei 101 (Taipei)
CN
Tower (Toronto)
KVLY-TV
Mast
(North Dakota)
Dubai Tower (Dubai)
818 m
Ostankino TV Tower, Moscow, Russia 540 m
Guangzhou New TV Tower, China 610 m
Tokyo Sky Tree, Japan 634 m
Notes: 29
29

## Slide 30
30
Upward lightning initiated from the 818-m tall tower
in Dubai
Upward Lightning Initiated by Ground-Based Objects
Notes: 30
30

## Slide 31
31
Positive and Bipolar Lightning
Discharges to Ground
Notes: 31

## Slide 32
Four types of lightning effectively lowering cloud charge to ground. Only the initial leader is shown for each type. In each lightning-type name given below the sketch, the direction of propagation of the leader and the polarity of the cloud charge effectively lowered to ground (not polarity of the initial leader) are indicated.
Types of Lightning Discharges: CGs
32
Notes: 32

## Slide 33
High-speed (1000 frames per second) video record of a positive flash
preceded by a cloud discharge that occurred on June 16, 2006 in China.
Courtesy of Dr. Xiangzhen Kong.
Positive and Bipolar Lightning Discharges to Ground
33
Notes: 33

## Slide 34
High-speed video record of a positive flash preceded by a cloud discharge that occurred on March 26, 2007 in Brazil. Interframe interval is 1 ms. Courtesy of Dr. M. Saba.
Positive and Bipolar Lightning Discharges to Ground
34
Notes: 34

## Slide 35
35
Positive lightning discharges have recently attracted considerable attention for a number of reasons including the following:
The highest recorded lightning currents (near 300 kA) and the largest charge transfers to ground (hundreds of coulombs or even more) are associated with positive lightning.
Positive lightning can be dominant type of cloud-to-ground lightning during the cold season, during the dissipating stage of a thunderstorm, and in some other situations.
Positive and Bipolar Lightning Discharges to Ground
Notes: 35

## Slide 36
Directly measured currents in three positive lightning discharges in Japan. The insets in the middle and bottom diagrams show the current on an expanded scale. The transferred charges, from top to bottom, are 330,180, and 400 C. Adapted from Goto and Narita (1995).
Positive and Bipolar Lightning Discharges to Ground
36
Notes: 36

## Slide 37
Lightning Damage to an Optical Fiber Ground Wire (OPGW)
Courtesy of Prof. Dr. Silverio Visacro Filho
37

## Slide 38
Although the overall percentage of positive lightning discharges is
relatively low, there are five situations, listed below that appear to
be conducive to the more frequent occurrence of such discharges.
The dissipating stage of an individual thunderstorm
Winter thunderstorms
Shallow clouds such as the trailing stratiform regions of mesoscale convective systems (MCSs)
Severe storms
Thunderclouds formed over forest fires or contaminated by smoke
Conditions conducive to the occurrence of positive lightning
38
Notes: 38

## Slide 39
Figure 5.2
The percentage of positive flashes over the contiguous United States as a function of month for each of the years 1995 through 1997. The minimum occurs in late summer and the maximum is in January-February. Adapted from Orville and Huffines (1999).
39
Notes: 39
5.2

## Slide 40
GIANT
BLUE
JET
PIXIES
TROLL
g
Varieties of Known (2009) Thunderstorm-Generated
Electrical Effects in the Upper Atmosphere
(Elaboration by D. Sentman of figure by Lyons et al. 2000)
40
20 km
Sprite
+CG
TLEs
Notes: 40

## Slide 41
Courtesy of Dr. D. Sentman
Sprites
41
Notes: 41

## Slide 42
Course Sections | Number of Lectures | HW Due (Can-vas) | Test (Honor-lock) | Section in Course Packet | Chapter/ Sections in Text (FOL)
Introduction | 1 |  |  |  | 
1. Types of lightning discharges and lightning terminology | 4 | HW1 01/25 | T1 01/27 | 1 | 1, App. 1, 4
2. Incidence of lightning to areas and structures | 4 | HW2 02/05 | T2 02/08 | 2 | 2, Sect. 9.3
3. Electrical structure of thunderstorm clouds | 6 | HW3 02/22 | T3 02/24 | 3 | 3, App. 2
4a. Properties of the negative lightning discharge to ground - I | 5 | HW4 03/08 | T4 03/10 | 4a | 4.1-4.3, 4.6, 4.10
4b. Properties of the negative lightning discharge to ground – II | 4 | HW5 03/19 | T5 03/22 | 4b | 4.4-4.5, 4.7-4.10, 9.3

## Slide 43
Conceptual cloud-charge-configurations/scenarios leading to production of downward positive lightning. Adapted from Nag and Rakov (2012).
43
Charge Configurations/Scenarios Leading to Production of Positive Lightning
Titled positive dipole
Unusually large lower positive charge region
Positive monopole
Negative in-cloud leader channel cut-off
Branching of in-cloud channel
Inverted dipole
(with additional lower negative charge region)
Positively-charged cloud region
Previously-formed in-cloud lightning channel

## Slide 44
A possible explanation of observed bipolar lightning currents. Currents of both polarities follow, in turn, the same channel to the ground, with negative charge transfer from the cloud charge region labeled “1” being followed by positive charge transfer from the charge region labeled “2”. Adapted from Narita et al. (1989)
44
Bipolar Lightning Discharges
1
2
Electrical charge structure of a convective cloud. Note pockets of positive and negative charge (numerous smaller encircled plus and minus signs) at different altitudes, while the net charge at the top of the cloud is positive and that at the bottom of the cloud it is negative.
_
+

## Slide 45
Global Electric Circuit
Electrosphere (σ >> ωε) is about 50 km above ground surface, forming a spherical capacitor. Potential difference V is about 300 kV, charge magnitude Q is about 0.5 MC, fair-weather current I is about 1 kA (10-12 A/m2). Capacitance C = Q/V = 1.7 F and the total resistance R = V/I = 300 Ω, so that τ = RC = 500 s (about 8 min).
Rain (positive charge moving down)
Corona (positive charge moving up)

## Slide 46
Sketches of overall-flash current records to illustrate different types of bipolar lightning discharges. RS=Return Stroke.
Bipolar Flashes – Types 1 and 2
46
Notes: 46

## Slide 47
Sketches of overall-flash current records to illustrate different types of bipolar lightning discharges (cont’d).
Bipolar Flashes – Types 3a and 3b
47
Notes: 47

## Slide 48
48
Portion of four-stroke bipolar flash #312 initiated from the 100-m Gaisberg tower, Austria. Adapted from Schulz and Diendorfer (2003).
Bipolar Flash - Type 3a (Upward Flash)
Notes: 48

## Slide 49
a Five changes from negative to positive and one change from positive to negative.
b Changes from negative to positive (Wada et al. , 1996a).
Observed polarity of currents in winter lightning in Japan (6 to 14% in summer)
Bipolar Flashes - Statistics
Source | Strike Object | Observation Period | Number of Positive (percent) | Number of Negative (percent) | Number of Bipolar (percent) | Total (percent)
Miyake et al. (1992) | 88-m weather observation tower at Kashiwazaki and 200-m stack at Fukui | 1978-1986 | 41 (33) | 78 (62) | 6a (5) | 125 (100)
Goto and Narita (1995) | 150-m meteorological tower at Maki | 1982-1993 | 25 (17) | 91 (63) | 29 (20) | 145 (100)
Wada et al. (1996a, b) | 200-m stack at Fukui | 1989-1994 | 4 (9) | 36 (80) | 5b (11) | 45 (100)
Nagai et al. (1996) | 500-kV Genden-Tsuruga transmission line tower | 1986-1992 | 1 (4) | 15 (63) | 8 (33) | 24 (100)
Wang et al. (2010, ICLP) | 100-m windmill and its 105-m protection tower at Uchinada | 2005-2009 | 8 (15) | 36 (70) | 8 (15) | 52 (100)
Notes: 49