## Slide 1
1
Rocket-and-wire triggered lightning

## Slide 2
It is a full-scale lightning discharge between a natural thundercloud and a designated point on ground that is artificially initiated using the so-called rocket-and-wire technique.
This technique involves the launching of a small rocket extending a thin wire (either grounded or ungrounded) toward the charged cloud overhead. In most respects the triggered lightning is a controllable analog of natural lightning. First lightning triggering was done in the U.S. in the 1960s over salt water.
2
What Is the Rocket-and-Wire Triggered
Lightning?

## Slide 3
Results of these experiments can serve
to understand better the physics of the lightning discharge,
to improve lightning protection schemes,
to evaluate the performance characteristics of lightning locating systems, and
to test the validity of lightning models.
3
What Can We Learn from Rocket-and-Wire
Triggered Lightning Experiments?

## Slide 4
Schematic illustration of the equipotential surfaces in the lowest 200 m and their interaction with a rocket extending a thin grounded wire which transfers ground potential to an altitude of about 150 m.
The equipotentials are concentrated geometrically near the tip of the rocket, which means that the electric field is enhanced there. When the field exceeds the critical breakdown value (a few hundred meters above ground), an upward leader is launched from the rocket tip.
Adapted from Willett (1992).
Instrumented
triggering facility
wire
4
4
Rocket-and-wire lightning triggering technique
Ez = -ΔV/Δz
Notes: 4

## Slide 5
5
Fiberglass rocket with a spool of Kevlar-coated copper wire.
ICLRT
Wire
spool
1-m
Rocket
Notes: 5

## Slide 6
Sequence of events in classical (grounded-wire) negative rocket-triggered lightning (rocket is needed only to extend the wire to a height of a few hundred meters). Adapted from Rakov (1999).
Leader/RS Sequence
Initial Stage
6
Rocket-and-wire lightning triggering technique
E-field

## Slide 7
Still picture (5-s exposure)
Wire Explosion Followed by the Initial Stage
Three Leader/Return Stroke Channels
Rocket Launcher
7
Optical Image of Rocket-Triggered Lightning Time-Resolved by the Action of Wind

## Slide 8
Natural
Triggered
Initial Stage (50 – 500 A)
~ 5 C
~ 1 C
~ 10 C
~ 1 C
~ 30 C
~ 10 C
~ 1 C
~ 1 C
8
Natural Lightning vs. Rocket-Triggered Lightning
Leader/return stroke sequences in triggered lightning are similar to subsequent leader/return stroke sequences in natural downward lightning.

## Slide 9
Rocket-Triggered Lightning
Altitude Triggering
9

## Slide 10
Photograph of a lightning flash triggered with a floating wire in Cachoera Paulista, Brazil on November 23, 2000. Courtesy Dr. Osmar Pinto Junior, INPE.
Altitude-triggered lightning
10
Upward positive leader
Downward negative leader
Exploded floating wire

## Slide 11
Lightning flashes initiated by airborne vehicles
Video frame of a lightning strike to an aircraft on takeoff from the Kamatsu Air Force Base, Japan, during winter. Courtesy of Z. I. Kawasaki.
11

## Slide 12
Overview of major triggered-lightning programs (also experiments in Germany, Indonesia, and Russia)
Experimental site
Height above
sea level, m
Years of operation
Wire material
Location of
wire spool
Selected
references
Saint Privat d’Allier, France
1100
1973- 1996
Steel or copper
Ground or rocket
Fieux et al. (1978), SPARG (1982)
Kahokugata, Hokuriku coast, Japan
0
1977-1985
Steel
Ground
Horii (1982), Kito et al. (1985)
Langmuir Laboratory, New Mexico
3230
1979-present
Steel
Ground
Hubert et al. (1984), Idone et al. (1984)
KSC, Florida (south of Melbourne, Florida in 1983)
0
1983-1991
Copper
Rocket
Eybert-Berard et al. (1986,1988),Willett(1992)
Okushishiku, Japan
930
1986-1998
Steel
Ground or rocket
Nakamura et al. (1991, 1992)
Seven different sites in China
Various
1989-present
Steel or copper
Ground or rocket
Liu et al. (1994),
Qie et al. (2007)
Fort McClellan, Alabama
190
1991-1995
Copper
Rocket
Fisher et al. (1993), Morris et al. (1994)
20-25
1993-present
Copper
Rocket
Uman et al. (1997),
570
1999-2007
Copper
Rocket
Saba et al. (2000, 2003),
Solorzano et al. (2002)
Rakov et al. (1998, 2004)
Camp Blanding, Florida
(>450 flashes; >100 papers)
Cachoeira Paulista, Brazil
12

## Slide 13
Lightning Triggering Sites in China
The first successful rocket-and-wire lightning triggering in China was conducted in 1977 by the Chinese Academy of Sciences (CAS).
More than 300 flashes were triggered in 7 different areas since then.
Two sites are presently operated by CAS and CMA (Chinese Meteorological Administration).
Conghua,
1998-2000
Binzou
2005-, CAS
Triggering Sites
Shanghai
1995
Nanchang,
1993-94
Beijing,1992-93
Gansu
1977,1989-92; 2001
Tibet, 2004
Binzhou,
2005-, CAS
Conghua,
2006-, CMA
Courtesy: Dr. Xiushu Qie, Chinese Academy of Sciences
13

## Slide 14
“Faraday cage” effect
Triggered lightning strike to a car with a live rabbit inside in Japan. Note flashovers across the tires and ground surface arcs. Courtesy of S. Sumi.
14

## Slide 15
15
Lightning triggering facility at Camp Blanding, Florida

## Slide 16: ICLRT at Camp Blanding, Florida (2009)

## Slide 17
Overview of the ICLRT, 2000 - 2007
The International Center for Lightning Research and Testing (ICLRT) at
Camp Blanding, Florida
17

## Slide 18
18
Photographs of lightning flashes triggered in 1997 at the ICLRT at Camp Blanding, Florida. Top, a distant view of a strike to the test runway; bottom, a close-up view of a strike to the test power system initiated from the 11-m high tower launcher.
ICLRT

## Slide 19
Still picture of a multiple-stroke flash triggered at Camp Blanding, Florida. This flash started a grass fire.
19
Notes: 19

## Slide 20
Anomalous Triggered Lightning Flash
ICLRT
20

## Slide 21
21
A lightning strike initiated in 1999 from the underground launcher at the center of a 70  70 m2 buried metallic grid
ICLRT
Notes: 21

## Slide 22
A lightning strike initiated in 2003 from the mobile launcher
ICLRT
22

## Slide 23
ICLRT
23
Mobile rocket launcher

## Slide 24
24
F0321-OFFICE-WIDE
Interaction of lightning with overhead power distribution lines
at Camp Blanding, Florida
Rocket launcher

## Slide 25
F0312-LC-NORMAL
25
Direct lightning strikes to the lightning protective system of a residential building at Camp Blanding, Florida
Notes: 25

## Slide 26
Concluding remarks
26
Results of triggered-lightning experiments have provided considerable insight into natural lightning processes that would not have been possible from studies of natural lightning due to its random occurrence in space and time.
Triggered-lightning experiments have contributed significantly to (a) testing the validity of various lightning models and (b) providing ground-truth data for testing the performance characteristics of lightning locating systems.
Triggered lightning is a very useful tool for studying the interaction of lightning with various objects and systems and testing lightning protection schemes.

## Slide 27
Camp Blanding, June 5, 2010, 3 strokes
27
→

## Slide 28
Camp Blanding, June 17, 2010, 8 strokes
28

## Slide 29
0401_LC_Tower_Normal
29
Notes: 29

## Slide 30
0401_LC_Tower_Slow
30
Notes: 30

## Slide 31
31
F0321-OFFICE-WIDE

## Slide 32
2011 ICLRT Site Layout

## Slide 33
33
The lightning-triggering facility at Camp Blanding, Florida, was established in 1993 by the Electric Power Research Institute (EPRI) and Power Technologies, Inc. (PTI). Since September 1994, the facility has been operated by the University of Florida (UF). Over 40 researchers (excluding UF faculty, students, and staff) from 15 countries representing 4 continents have performed experiments at Camp Blanding concerned with various aspects of atmospheric electricity, lightning, and lightning protection.
Since 1995, the Camp Blanding facility has been referred to as the International Center for Lightning Research and Testing (ICLRT). Presently it is jointly operated by UF and Florida Institute of Technology (FIT) and additionally includes the Lightning Observatory in Gainesville (LOG).
The International Center for Lightning Research and Testing (ICLRT) at
Camp Blanding, Florida (http://www.lightning.ece.ufl.edu)

## Slide 34
34
The International Center for Lightning Research and Testing (ICLRT) at
Camp Blanding, Florida (http://www.lightning.ece.ufl.edu)
Australia: M. Darveniza
Austria: G. Diendorfer,
M. Mair
Canada: H. Mercure,
S. Cyr
France: A. Eybert-Berard,
J. P. Berlandis,
B. Bador,
P. Lalande,
P. Laroche,
S. Chauzy,
S. Soula
Germany: J. Kallweit,
J. Schoene
Iran: R. Moini
Italy: C. A. Nucci,
S. Guerrieri,
M. Paolone
Japan: D. Wang,
M. Miki,
S. Yoshida
Norway: H. Hoidalen
Poland: K. Chrzan,
G. Maslowski
Russia: V. Lebedev
Sri Lanka: P. Liyanage
Sweden: V. Cooray,
M. Rahman
Switzerland: F. Rachidi,
M. Rubinstein,
E. Petrache
USA: R. Fisher,
(partial) G. Schnetzer,
C. Weidman,
V. Idone,
W. Beasley,
H. Christian,
E.P. Krider

## Slide 35
1993 - 2014 Triggered-Lightning Experiments at Camp Blanding, Florida
Year(s) | Rocket Launchers Used | Total Flashes Triggered | Flashes With Return Strokes | Positive or Bipolar Flashes | Time Period
1993 | 1 | 32 | 22 | - | June 7 – Sept. 21
1994 | 2 | 15 | 11 | - | August 4 – Sept.
1995 | 2 | 14 | 13 | - | June 25 – August 19
1996 | 2 | 30 | 25 | - | June 20 – Sept. 11
1997 | 4 | 48 | 28 | 1 | May 24 – Sept. 26
1998 | 3 | 34 | 27 | - | May 15, July 24 – Sept. 30
1999 | 2 | 30 | 22 | 1 | Jan 23, June 26 – Sept. 27
2000 | 2 | 30 | 27 | - | June 12 – Sept. 6
2001 | 2 | 23 | 11 | - | July 13 – Sept. 5
2002 | 2 | 19 | 14 | - | July 9 – Sept. 13
2003 | 2 | 24 | 12 | 1 | June 30 – Aug. 15
2004 | 1 | 5 | 3 | - | June 23 – July 24

## Slide 36
1993 - 2014 Triggered-Lightning Experiments at Camp Blanding, Florida
Year(s) | Rocket Launchers Used | Total Flashes Triggered | Flashes With Return Strokes | Positive or Bipolar Flashes | Time Period
2005 | 2 | 11 | 8 | - | July 2 – August 5
2007 | 1 | 2 | 1 | - | July 13 – July 31
2008 | 1 | 11 | 7 | 1 | May 16 – Oct. 9
2009 | 1 | 26 | 18 | 2 | Febr. 19 – August 18
2010 | 2 | 13 | 12 | - | June 5 – Sept. 27
2011 | 1 | 16 | 12 | 1 | Jan. 25 – Aug. 18
2012 | 1 | 26 | 19 | 1 | May 15 – Aug. 21
2013 | 1 | 20 | 12 | - | May 20 – Aug. 17
2014 | 1 | 27 | 19 | - | May 29 – Aug. 15
1993-2014 (21* years) |  | 456 | 323 (71%) | 8 (1.8%) | * There was no lightning triggering in 2006