## Slide 1
1
3. Electrical Structure of
Thunderstorm Clouds

## Slide 2
Course Sections | Number of Lectures | HW Due (Can-vas) | Test (Honor-lock) | Section in Course Packet | Chapter/ Sections in Text (FOL)
Introduction | 1 |  |  |  | 
1. Types of lightning discharges and lightning terminology | 4 | HW1 01/25 | T1 01/27 | 1 | 1, App. 1, 4
2. Incidence of lightning to areas and structures | 4 | HW2 02/05 | T2 02/08 | 2 | 2, Sect. 9.3
3. Electrical structure of thunderstorm clouds | 6 | HW3 02/22 | T3 02/24 | 3 | 3, App. 2
4a. Properties of the negative lightning discharge to ground - I | 5 | HW4 03/08 | T4 03/10 | 4a | 4.1-4.3, 4.6, 4.10
4b. Properties of the negative lightning discharge to ground – II | 4 | HW5 03/19 | T5 03/22 | 4b | 4.4-4.5, 4.7-4.10, 9.3

## Slide 3
EEL 5490/4495
LIGHTNING
Spring 2021
Rakov, V.A. Fundamentals of Lightning (FOL), Cambridge University Press, 2016
Rakov, V.A., Lightning, Lecture Slides (LS) (available at http://www.rakov.ece.ufl.edu/teaching/5490/5490.html)
HOME ASSIGNMENT 3
(Electrical structure of thunderstorm clouds)
Due: Febr. 22, 2021 (before 1:55 p.m.)
Reading: FOL, Ch. 3, App. 2, and LS, Section 3
Problems (from FOL): 3.5 - 25%
3.6 - 25%
3.7 - 25%
3.8 - 25%

## Slide 4
An isolated thundercloud in the central New Mexico, with rudimentary indication of how electric charge is thought to be distributed and around the thundercloud, as inferred from the remote and in situ observations. Adapted from Krehbiel (1986).
LPCR →
Corona→
Negative screening layer
Main
positive
Main
negative

## Slide 5
Corona is a non-self-propagating discharge confined to the vicinity of a sharp, E-field enhancing object. It radiates mostly in UV and is very faint (never seen by most people), although it always occurs during thunderstorms.

## Slide 6: Corona discharge from barbed wire
Barbed wire subjected to a positive dc voltage of 400-kV magnitude in laboratory. Adapted from Gary (1994).

## Slide 7: Corona discharge from trees
(Left) 1200-kV ac transmission line in Lyons, Oregon. Douglas fir trees at the edge of the line right-of-way are seen on the left side of the picture. Typical measured ground-level electric field maxima were 7 to 9 kV/m. (Right) Corona on a Douglas fir tree located about 12 m from conductors of the line. Photograph was taken with a night viewing (image enhancement) device. Needle tip burns were observed. Adapted from Rogers et al. (1979).
Phase conductor
(8-conductor bundle) of a 1.2-MV transmission line

## Slide 8: St. Elmo’s fire (corona) on a ship

## Slide 9: Corona from a human hand
Corona discharge from a human hand in laboratory (Istra, Russia). Electric field was produced by a cloud of negatively-charged water droplets. The hand was at a distance of 3 to 5 m from the cloud edge. Courtesy of Dr. A. Kostinskiy.

## Slide 10
Cloud of charged
water droplets

## Slide 11
Cloud of charged
water droplets
↙

## Slide 12
Overhead thundercloud

## Slide 13
Overhead thundercloud
Safety Tip

## Slide 14
An isolated thundercloud in the central New Mexico, with rudimentary indication of how electric charge is thought to be distributed and around the thundercloud, as inferred from the remote and in situ observations. Adapted from Krehbiel (1986).

## Slide 15
15
15
A vertical tripole representing the idealized gross charge structure of a thundercloud. The negative screening layer charges at the cloud top and the positive corona space charge produced at ground are ignored here.
In order to compute E-fields, we will need to use (1) Coulomb’s Law, (2) the method of images, and (3) the principle of superposition.
Cloud Charge Structure and Mechanisms of Cloud Electrification
Notes: 3.2a

## Slide 16
Atmospheric electricity (AE) sign convention
600-ms full scale
10 min per division

## Slide 17
17
17
Electric field at the ground about 5 km from a small storm near Langmuir Laboratory, New Mexico, on 3 August 1984. An upward-directed electric field is defined as positive (according to the physics sign convention). The large pulses superimposed on the rising portion of the overall electric field waveform are due to lightning. Adapted from Krehbiel (1986).
Cloud Charge Structure and Mechanisms of Cloud Electrification
Fair-weather field
Thunderstorm field
Physics sign convention
5 min per division
Notes: 3.3

## Slide 18
18
18
A vertical tripole representing the idealized gross charge structure of a thundercloud. The negative screening layer charges at the cloud top and the positive corona space charge produced at ground are ignored here.
In order to compute E-fields, we will need to use (1) Coulomb’s Law, (2) the method of images, and (3) the principle of superposition.
Cloud Charge Structure and Mechanisms of Cloud Electrification
Notes: 3.2a

## Slide 20: Recommended Empirical Formulas
Ground Flash density, km-2 yr-2 :
Ng = 0.04 TD1.25 (Ng =0.1 TD for rough estimates)
Ng = 0.054 TH1.1 (Ng =0.05 TH for rough estimates)
Lightning incidence to towers ( for Hs> 20 m), yr-1 :
N = 24 x 10-6 Hs2.05 Ng, where Hs is in meters and Ng is in km-2 yr-1
Equivalent attractive radius (distance), m:
Ra =14 Hs 0.6 , where Hs≤ 100 m (Ra = 2Hs for rough estimates)
Percentage of upward flashes, % :
Pu = 52.8 ln Hs – 230, where Hs is in meters
71%
N = 28 per year
(20 + 8)

## Slide 21
According to the IEEE Std 1243,
and the transmission-line flash collection rate, Ns (in strikes/100 km/yr) is
where h and b are in meters and Ng in flashes/km2/yr (L = 100 km).
(Ra = 2h for rough estimates)

## Slide 22
40 m
30 m
20 m
10 m
10 m
10 m
Attractive area of an isolated 10 m x 20 m x 5 m house (Ng = 4 km-2 yr-1)
10 m
5 m
20 m
A
(attractive area of the house)
N
Poisson probability distribution:
p(n) = (Zn/n!)exp(-Z), where Z = ANgT

## Slide 23
Characteris-tics |  |  | LFC | LLS | Satellite Optical Detectors
Coverage | Global | Global | Regional | Regional and Global | Global
Long-term Data | Yes | Yes | Limited | Limited | Limited
Identification of CGs | No | No | Yes | Yes | No
Accuracy in estimating | Low | Low | Low | Good | Low
Characteris-tics |  |  | LFC | LLS | Satellite Optical Detectors
Coverage | Global | Global | Regional | Regional and Global | Global
Long-term Data | Yes | Yes | Limited | Limited | Limited
Identification of CGs | No | No | Yes | Yes | No
 | Low | Low | Low | Good | Low
4 (25%).
In no less than one-half but no more than one page discuss in your own words advantages and disadvantages of using TD, TH, lightning flash counters, lightning locating systems, and satellite optical detectors for estimating ground flash density.

## Slide 24
24
24
Method of images for finding the electric field due to a negative point charge above a perfectly conducting ground at a field point located at the ground surface.
Cloud Charge Structure and Mechanisms of Cloud Electrification
(H2 + r2)3/2 = R3
H/R = sin α
k = Q /(2πε0)
Notes: 3.2b

## Slide 25
25
25
A vertical tripole representing the idealized gross charge structure of a thundercloud. The negative screening layer charges at the cloud top and the positive corona space charge produced at ground are ignored here.
In order to compute E-fields, we will need to use (1) Coulomb’s Law, (2) the method of images, and (3) the principle of superposition.
Cloud Charge Structure and Mechanisms of Cloud Electrification
Notes: 3.2a

## Slide 26
26
26
A vertical tripole representing the idealized gross charge structure of a thundercloud. The negative screening layer charges at the cloud top and the positive corona space charge produced at ground are ignored here.
In order to compute E-fields, we will need to use (1) Coulomb’s Law, (2) the method of images, and (3) the principle of superposition.
Cloud Charge Structure and Mechanisms of Cloud Electrification
ΔE due to removal of QN (-CG) is equal to the negative of E-field due to QN (ΔE = Efinal - Einitial)
Notes: 3.2a

## Slide 27
27
27
The electric field at ground due to the vertical tripole, labeled “Total”, as a function of the distance from the axis of the tripole. Also shown are the contributions to the total electric field from the three individual charges of the tripole. An upward directed electric field is defined as positive (according to the physics sign convention).
Cloud Charge Structure and Mechanisms of Cloud Electrification
Physics sign
convention
QN
QP
QLP
Total
E
Notes: 3.2c

## Slide 28
28
Electric field change at ground, due to the total removal of the negative charge of the vertical tripole via a cloud-to-ground discharge, as a function of distance from the axis of the tripole. Note that the electric field change at all distances is negative. [The CG neutralized only 1 of the 3 charges]
Electric field change at ground, due to the total removal of the negative and upper positive charges of the vertical tripole via a cloud discharge, as a function of distance from the axis of the tripole. Note that the electric field change at close distances is negative, but at far distances it is positive. [The IC neutralized only 2 of the 3 charges]
Cloud Charge Structure and Mechanisms of Cloud Electrification
Electric Field Change Due to Negative Cloud-to-Ground Discharge
Electric Field Change Due
to a Cloud Discharge
Distance, km
Distance, km
Electric Field Change, kV/m
Electric Field Change, kV/m
Physics sign convention
No reversal
distance
D0 = 13 km
Notes: 3.2d & 3.2 e

## Slide 29: Electric field changes (ΔE = Efinal - Einitial)
Overall electric field change for a four-stroke flash with a long continuing current following the third stroke. The flash occurred in Florida on July 27, 1979 at a distance of 6.5 km. Microsecond-scale initial electric field peaks are not resolved in this Figure, but their values Ep (normalized to 100 km) are given. Positive electric field change (atmospheric electricity sign convention) deflects upward. Adapted from Rakov and Uman (1990a).
Continuing Current Electric Field Change
4th Stroke Following Continuing Current Interval
3rd Stroke Initiating Continuing Current
2nd Stroke Preceding Stroke Initiating Continuing Current
1st Stroke

## Slide 30
Summary of different models used to infer cloud charges neutralized by lightning
discharges based on multiple-station measurements of ΔE. The monopole model
(a) is applied to cloud-to-ground strokes, flashes, or continuing currents, while the
three versions of the dipole model (b), (c), and (d) are used to represent cloud
discharges, including the preliminary breakdown in CG flashes. In the point-dipole
model, Δp is the dipole moment change, and Δl is the distance (unresolved in the
model) between Q+ and Q-, which should be much smaller than the inclined distance
R to either of them.

## Slide 31: Electric field changes (ΔE = Efinal - Einitial)
Overall electric field change for a four-stroke flash with a long continuing current following the third stroke. The flash occurred in Florida on July 27, 1979 at a distance of 6.5 km. Microsecond-scale initial electric field peaks are not resolved in this Figure, but their values Ep (normalized to 100 km) are given. Positive electric field change (atmospheric electricity sign convention) deflects upward. Adapted from Rakov and Uman (1990a).
Continuing Current Electric Field Change
4th Stroke Following Continuing Current Interval
3rd Stroke Initiating Continuing Current
2nd Stroke Preceding Stroke Initiating Continuing Current
1st Stroke
ΔEcc
ΔE2
ΔE1

## Slide 32
E-fields of a 5-stroke flash measured at 8 stations in NM
Inferred cloud charged neutralized by the 5 strokes
Preliminary breakdown
(A + B)

## Slide 33
Inferred charges neutralized by individual strokes and continuing currents in 4 -CGs in New Mexico
Elevation varies from 4.5 to 6.0 km (one exception 3.6 km)
Temperature varies from -9 to -17o C (mixed-phase region)
20 nC/m3

## Slide 34
An isolated thundercloud in the central New Mexico, with rudimentary indication of how electric charge is thought to be distributed and around the thundercloud, as inferred from the remote and in situ observations. Adapted from Krehbiel (1986).
LPCR →
Corona→
Negative screening layer
Main
positive
Main
negative

## Slide 35
35
Negative charges (circles) neutralized by ground flashes, and point-dipole charge moments (arrows) describing the effective positive charge transfer by cloud flashes as a function of time for a portion of a Florida storm. The numbers in the circles give the magnitudes of the neutralized charges in coulombs. In cloud flashes, negative charge was effectively transported in the direction opposite to that of the arrow to neutralize a positive charge of equal magnitude. The dot in the middle of each arrow represents the apparent single location of these two charges.
Cloud Charge Structure and Mechanisms of Cloud Electrification
35
Point-charge and point-dipole solutions
Notes: 3.6

## Slide 37
The main negative charge appears to remain at approximately constant altitude (about 7 km) and temperature level (about -15o C) as the thunderstorm grows.
Inferred heights of charges neutralized by 13 ICs and 2 CGs in a small Florida thunderstorm (8-minute total duration)

## Slide 38
38
The location, shown by the small irregular contours inside the cloud boundaries, of ground flash charge sources observed in summer thunderstorms in Florida and New Mexico and in winter thunderstorms in Japan, using simultaneous measurements of electric field at a number of ground stations. Adapted from Krehbiel (1986).
Cloud Charge Structure and Mechanisms of Cloud Electrification
38
Notes: 3.7

## Slide 39
Gauss Law
Cloud charge structure from in-situ measurements (New Mexico)
One-dimensional approximation to Gauss Law:

## Slide 40
40
Balloon measurements of the vertical electric field inside a small Alabama thunderstorm. An upward-directed electric field is defined as positive. The values of the inferred average charge density (in nC m-3) are shown on the right. The field profile is indicative of a “classical” vertical tripole with an upper negative screening layer. Adapted from Marshall and Rust (1991).
Cloud Charge Structure and Mechanisms of Cloud Electrification
Gauss Law
40
Notes: 3.10

## Slide 41: Cloud electrical environment
41
Fig. 3a of Gurevich and Zybin (2005, Physics Today).
Electric field profiles in thunderclouds. Four examples of balloon measurements of the vertical electric field in thunderclouds are presented by color curves, adapted from Marshall et al. (1995).
Also shown is the calculated runaway breakdown critical electric field Ec, which decreases with height because of decreasing air density. “L” denotes lightning discharges.
At 6 km
Ec ~ 105 V/m (100 kV/m)
Eb ~ 106 V/m (1000 kV/m)
(conventional breakdown electric field)
Notes: 41

## Slide 42
42
Charge transfer by collision in the graupel-ice mechanism of cloud electrification. It is assumed that the reversal temperature TR is -15º C and that it occurs at a height of 6 km.
Cloud Charge Structure and Mechanisms of Cloud Electrification
42
Reversal
temperature
Notes: 3.13

## Slide 43
43
The charge acquired by a riming hail particle (simulated by an ice-covered cylindrical metal rod with diameter 0.5 cm) during collisions with 50 μm ice crystals, as a function of the temperature of the rime in the laboratory. The velocity of impact was 2.9 m s-1. The cloud liquid water content was approximately 1 g m-1, and the mean diameter of the water droplets was 10 μm. Adapted from Jayaratne et al. (1983).
[Charge on the vertical scale is in femtocoulombs; 1 fC = 10-15 C]
Cloud Charge Structure and Mechanisms of Cloud Electrification
43
Reversal temperature is
between -19o C and -20o C
Notes: 3.14

## Slide 44
EEL 5490/4495
LIGHTNING
Spring 2021
Rakov, V.A. Fundamentals of Lightning (FOL), Cambridge University Press, 2016
Rakov, V.A., Lightning, Lecture Slides (LS) (available at http://www.rakov.ece.ufl.edu/teaching/5490/5490.html)
HOME ASSIGNMENT 3
(Electrical structure of thunderstorm clouds)
Due: Febr. 22, 2021 (before 1:55 p.m.)
Reading: FOL, Ch. 3, App. 2, and LS, Section 3
Problems (from FOL): 3.5 - 25%
3.6 - 25%
3.7 - 25%
3.8 - 25%

## Slide 45
Illustration of the convection mechanism (external sources of charge and organized convection) of cloud electrification. Adapted from MacGorman and Rust (1998).
It is unlikely that corona at ground is the source of the main positive charge region, but it can contribute significantly to the lower positive charge region (LPCR) (Chauzy and Soula, 1999).
Mechanisms of Cloud Electrification

## Slide 46
Role of Lower Positive Charge Region in Facilitating Different Types of Lightning
Left panel is a schematic illustration (not to scale) of electric field enhancement and reduction effects of the lower positive charge region (+QLP) below the main negative charge region (-QN). The main positive charge region is not shown. Arrows indicate the direction of vertical components of electric field vectors. The total electric field is enhanced, (EN + ELP), between the negative and positive charge regions and reduced, (EN – ELP), below the positive charge region.
Right panel shows (a) schematic representation of preliminary breakdown stepping process in negative ground flashes. Negatively-sloped arrow indicates the overall downward extension of negatively charged channel through the LPCR. Three steps giving rise to current (and light) pulses are shown. Each current pulse originates at the tip of downward-extending channel and propagates upward (positively-sloped arrows). (b) A sketch of expected electric field record of resultant wideband PB pulse train.
46

## Slide 47
The left panels, A-D, schematically show four types of lightning that may arise depending upon the magnitude of the LPCR. The charge configuration in each of the scenarios represents only its vertical profile (no lateral boundaries are shown). Arrows indicate the direction of propagation of negative leader. The corresponding examples of expected electric field signatures are shown in the right panel.
The field waveforms are from four different thunderstorms recorded at some tens of kilometers in Gainesville, Florida, using the same instrumentation with a decay time constant of 10 ms. PB = preliminary breakdown pulse train, RS = return-stroke waveform. Adapted from Nag and Rakov (2009).
Notes: 47